## Slide 1: ChannelFinder setup on vclx4
Jimmy You
Mar. 2022
https://www-bd.fnal.gov/controls/micro_p/channelfinder/channelfinder_setup.pptx

## Slide 2
Deployment Diagram

## Slide 3: Compoment: RecSync/RecCaster
https://github.com/ChannelFinder/recsync
EPICS module
Listen to UDP broadcast at port 5049
Forward PV and Field “alias” and “info” with TCP
test.db
record(longin, “test:li") {
alias(“test:lix1")
alias(“test:lix2")
info("test", "testing")
}
st.cmd
## Register all support components
dbLoadDatabase("../../dbd/demo.dbd",0,0)
demo_registerRecordDeviceDriver(pdbbase)
var(reccastTimeout, 5.0)
var(reccastMaxHoldoff, 5.0)
epicsEnvSet("IOCNAME", "myioc")
epicsEnvSet("ENGINEER", "myself")
epicsEnvSet("LOCATION", "myplace")

## Slide 4: Compoment: RecSync/RecCeiver
https://github.com/ChannelFinder/recsync
Python with Twisted package and pyCFClient(https://github.com/ChannelFinder/pyCFClient)
  twistd -n recceiver -f cf.conf
UDP broadcast to port 5049, with TCP callback info
Receive PV from IOC/RecCaster at the TCP port
Forward PV with pyCFClient API to ChannelFinder Web Service
Configuration:
  cf.conf
    addrlist = 255.255.255.255:5049
    infotags = test hello
    alias = on
  channelfinderapi.conf
    BaseURL=http://vclx4:8088/ChannelFinder

## Slide 5: Compoment: ChannelFinder Web Service
https://github.com/ChannelFinder/ChannelFinderService
SpringBoot/Tomcat
Receive PV from RecCeiver via HTTP REST API
Use ElasticSearch Index DB
  Three indices: mapping_definitions.sh
    channelfinder/cf_channel
    properties/cf_property
    tags/cf_tag
Use embedded LDAP for authentication, configured in cf.ldif
Configuration: app.properties; cf.ldif
  server.http.port=8088
  logging.file=${java.io.tmpdir}/channelfinder.log
  elasticsearch.network.host: centry.fnal.gov
  elasticsearch.http.port: 9200
Run
  nohup java --add-exports=java.naming/com.sun.jndi.ldap=ALL-UNNAMED
  -Dspring.config.location=file:./target/classes/app.properties
  -jar target/ChannelFinder-4.0.0.jar > /dev/null 2>&1 &

## Slide 6: Compoment: ChannelFinder Web Service
Human interfaces
curl http://vclx4:8088/ChannelFinder/resources/channels?test=testing
http://vclx4:8088/
Phoebus Channel View
  q: * test=testing
  q: FNAL*DEW*

## Slide 7: Phoebus display builder and web runtime
Display Builder
  https://github.com/ControlSystemStudio/phoebus
  Java based GUI tool to build control interface
  Run: phoebus.sh
  Configuration: settings.ini
    org.phoebus.channelfinder/serviceURL=http://vclx4:8088/ChannelFinder
  BOB repo: vclx4:/usr/local/epics/Config/CSS/PIP2TS/HB650
Web Runtime
  https://github.com/ornl-epics/dbwr
  https://github.com/ornl-epics/pvws
  Tomcat with dbwr.war and pvws.war
  Run: ~/apache-tomcat-9.0.58/bin/startup.sh
  Configuration: bin/setenv.sh
    export EPICS_CA_ADDR_LIST=131.225.120.227:6722
    export PV_WRITE_SUPPORT=true
  http://vclx4:8080/dbwr/view.jsp?display=http://vclx4:8080/PIP2TS/HB650/HB650cryostat.bob
  BOB update/sync:
    cp –rp /usr/local/epics/Config/CSS/PIP2TS ~/apache-tomcat-9.0.58/webapps/ROOT

## Slide 8: Debug/Howto/Troubleshooting/log
RecSync/Reccaster/RecCeiver/demoIOC
  code "fix“: __init__.py: remove reactor, pollreactor.install()
  Enable debug: cf.conf: loglevel=DEBUG
  debug with alternative port(5049 -> 5050): update announce.py and cf.conf and caster.h
  python setup.jy install
ChannelFinder Web Runtime (app.properties)
  logging.file=${java.io.tmpdir}/channelfinder.log
  logging.level.org.elasticsearch.client.RestClient=ERROR
  logging.level.gov.bnl.channelfinder.ChannelManager.audit=WARN
  server.http.port=8088
  Test
  curl --basic -u x:x -H 'Content-Type: application/json' -X PUT -d '{"name":"foo", "owner":“x"}’ http://vclx4:8088/ChannelFinder/resources/tags/foo
  curl http://vclx4:8088/ChannelFinder/resources/tags/foo
Copy file:
  pscp -r -p -load via_nc_proxy pvws.war youj@clx28:
TCP tunneling
  plink -N -T -no-antispoof -L 8088:vclx4.fnal.gov:8088 youj@outland.fnal.gov
Install python package on vclx4, via outback
  ssh -D:1080 outback
  proxychains pip3 install twisted