Central ACNET Task List Maintenance
-----------------------------------

There are three files which must be modified when tasks
are added or deleted from the central VAX task lists:
ACNETBOOT.COM, OPRACNET.COM, and ACNETSHOW.DAT.
In some cases, ASHUTDOWN.COM may also need to be modified.

ACNETBOOT.COM
-------------

The master copy of this file is in DWIN$DISK:[DWIN.ACNET.COM].
This is the DCL command file which starts various ACNET tasks
on the central VAXes (both development and operational clusters).
When you modify this file, don't forget to add a line to the
modification history at the end of the file.

Copy this file to SYS$COMMON:[ACNET] on both central clusters.
One file serves all member nodes on a single cluster.

DO NOT COPY this file to the console download area!

OPRACNET.COM
------------

The master copy of this file is in DWIN$DISK:[DWIN.ACNET.COM].
This is the DCL command file which provides operator console
support for the various ACNET commands.  In particular, it
validates any ACNET task name given in an operator command.
This validation occurs in the DCL subroutine CHECK_SUBSYS:.

Copy this file to SYS$COMMON:[SYSMGR.OPERATOR] on both central
clusters.  One file serves all member nodes on a single cluster.

DO NOT COPY this file to the console download area!

ACNETSHOW.DAT
-------------

The master copy of this file is in DWIN$DISK:[DWIN.ACNET.NETUTL].
This is the control file for the ACNETSHOW command which performs
finger commands on the various operational nodes.  The structure
of this text file is very simple.  There is one group for each
operational node.  A line containing "---" separates the various
groups.  The first line of each group is the node name, and
following lines contain the tasks for that node.

Copy this file to SYS$COMMON:[ACNET] on both central clusters.
One file serves all member nodes on a single cluster.

DO copy this file to DWIN$DISK:[DWIN.DOWNLOAD.ACNET] since the
ACNETSHOW command is supported on consoles.

ASHUTDOWN.COM
-------------

The master copy of this file is in DWIN$DISK:[DWIN.ACNET.COM].
This is the DCL command file which is invoked whenever
ACNET is shutdown on any central VAX.  Some tasks require
special shutdown procedures which are invoked by this command
file,  but if a particular task is not referenced in this command
file, it will be FORCEXITed by the STPNETUSE program.

Copy this file to SYS$COMMON:[ACNET] on both central clusters.
One file serves all member nodes on a single cluster.

DO NOT COPY this file to the console download area!